## Slide 1
Ph.D. Proposal Plan
Dec. 15th
Jongman Seo
Advisor: Seungmoon Choi
Haptics and Virtual Reality Lab.
Pohang University of Science and Technology (POSTECH)
Audio-Based Haptic Effects Synthesis for 4D Films

## Slide 2
Research History
2009~2013
Vibrotactile Flows on a Mobile Device
2014~2016
Audio-Based Haptic Effects Synthesis for 4D Films

## Slide 3
Research Overview
4D Film: visual + auditory + haptic
- Motion Chair, Vibration, Wind, ...
- The main focus of this research is vibration.
4D Fiims and
Haptic Effects
Auditory-to-vibrotactile conversion assuring perceptual consistency between modalities
Surround sound (multi-channel audio)
Audio Analysis

## Slide 4
Goal of This Research
Long-Term Goal
- Automatically generating tactile effects for the given movie scene by analyzing its audio signal
Short-Term Goals
Event capturing (likely to be rendered in haptic)
Providing tactile effects having similar perceptual feeling of audio signal by studying auditory-to-tactile conversion
Providing spatiotemporal tactile effects to emphasize spatial variations of events by analyzing multi-channel audio signal

## Slide 5
1. Event Detection
1-1. Detection algorithm using psychoacoustic metrics
1-2. Quantitative Evaluation
Research Progress
Black: Finished
Purple: Planned
2. Auditory-to-tactile conversion
2-1. Compensation method for auditory-to-vibrotactile conversion transparent to perception
2-2. Qualitative Evaluation
3. Multi-channel audio
3-1. Source localization and spatiotemporal haptic rendering method
3-2. Qualitative Evaluation

## Slide 6
Event Detection

## Slide 7
[gunshot, explosion], [collision], [exterior/interior vibration]
voice, background music
Events in Movie
Psychoacoustic
Metrics
( = Sound quality metrics)
Depend on Perceptual nature of the sound
Voice Removal
Done at audio recording level by removing the ‘Center’ channel, which contains voice
{Loudness, roughness, sharpness, booming}
Using psychoacoustic metrics is easy to detect events
i.e.) High value of sharpness when gunshot occurs

## Slide 8
Evaluation
of Event Detection
Intensity Model
    = Loudness, =Roughness, =sharpness,
    =booming, = volume parameter, = offset
 | Lee’s model (2013) |  | This model
Test set | Movie | Movie + voice | Movie + voice
Hit Rate | 90.5% | 90% | 85.6%
False Alarm | 20.5% | 40% | 27.5%

## Slide 9
Auditory-to-Tactile Conversion

## Slide 10
Perceptual intensity of
[auditory signal tactile signal]
Ploblems
Conversion Process
Relatively weak

## Slide 11
Feed-forward compensator to compensate for the effects of both tactile device and mechanoreceptor systems
Solves
: frequency response of tactile device
is the absolute threshold
Notes: AL 실험으로 구한 내용 생략

## Slide 12
Results
Original audio signal
Perceived intensity
after conversion
without compensation
Perceived intensity
after conversion
with compensation

## Slide 13
Multi-Channel Audio Analysis for Tactile Rendering

## Slide 14
Cross-power Spectrum Phase (CSP) Analysis
- A binaural hearing approach
- Fourier transform of cross correlation function between signals
- , : two different signal)
- Delay
-
3D Source Localization
(Estimation of the source position)

## Slide 15
Input signal: x(n), x(n+1000)
Output of CSP has the maximum value at n=1000
Results of
Delay Estimation
Input
CSP

## Slide 16
Using 4 channels of 5.1 channel
Front Left/Right
Side (Back) Left/Right
Center, LFE
Source Localization of 5.1 channel
Standard simplex optimization scheme
=
, c: sound speed, delay

## Slide 17
Using pad-type tactile device
Weight function multiplication for emphasizing spatial variation
Spatiotemporal Haptic Rendering
w1(t), …, w6(t)

## Slide 18
Plan
1. Event Detection
2. Auditory-to-tactile conversion
2-1. Compensation method
3. Multi-channel audio
3-1. Haptic rendering by analyzing 5.1 channel
3-1-1. Source localization
3-1-2. Hardware
3-1-3. Rendering algorithm
2-2. Qualitative evaluation
Improvement
Improvement
3-1-4. Qualitative evaluation
3-2. Haptic rendering by analyzing VR sound (360˚)